## Slide 1: EEM312 Laboratory
Lab assistants are: Dilara Değerliyurt–Süleyman Burak Çelik
Labs are divided into two sections (same as course sections). Verify your section as soon as possible.
Lab homepage: http://www.baskent.edu.tr/~ddegerliyurt
http://www.baskent.edu.tr/~sbcelik
If necessary, our document open password is 312lab

## Slide 2: EEM312 Laboratory
Contents of the lab
  Rise time, fall time, noise margin and delay measurements both in HW and SW labs
  Datasheet comparisons with the real measurements
  Regenerative property of logic gates
  Ring oscillators
  Diodes and diode based logic gates
  MOSFET models
  Mosfets and measurements and comparisons
  NMOS PMOS CMOS comparisons
  Power dissipation of inverters
  Domino logic implementation in Spice
  Pass transistors logic implementations
  Transmission gates and logics

## Slide 3: WinSpice
Circuit Simulation Program

## Slide 4: INTRODUCTION
WinSpice3 is a general-purpose circuit simulation program for non-linear DC, non-linear transient, and linear AC analyses
Circuits may contain resistors, capacitors, inductors, mutual inductors, independent voltage and current sources, four types of dependent sources, lossless and lossy transmission lines, switches, uniform distributed RC lines, and the four most common semiconductor devices: diodes, BJTs, JFETs, and MOSFETs

## Slide 5: INTRODUCTION
Installation:
  You may download program at
  http://www.baskent.edu.tr/~ddegerliyurt
  Follow the links for the related materials

## Slide 7: TYPES OF ANALYSIS
DC Analysis
AC Small-Signal Analysis
Transient Analysis
Pole-Zero Analysis
Small-Signal Distortion Analysis
Sensitivity Analysis
Noise Analysis
Analysis At Different Temperatures

## Slide 8: Writing WinSpice
WinSpice Deck/Netlist is a text description of a circuit consists of the following parts
Header
Circuit connections
Subcircuit descriptions (if needed)
Model descriptions (if needed – usually only for
transistors)
Analyses to be performed
Outputs to be saved / displayed

## Slide 11: Pulse
PULSE(V2 V1 TD TR TF PW PER)
EX:
VIN 3 0 PULSE(-1 1 2NS 2NS 2NS 50NS 100NS)
parameter | default value | units
V1 (initial value) |  | Volts or Amps
V2 (pulsed value) |  | Volts or Amps
TD (delay time) | 0.0 | seconds
TR (rise time) | TSTEP | seconds
TF (fall time) | TSTEP | seconds
PW (pulse width) | TSTOP | seconds
PER(period) | TSTOP | seconds